## Slide 1: Years-Long Image Broadcast using Bluetooth Low Energy Beacons
Chong Shao
Notes: I will talk about the project we did at UNC chapel hill
The title is …
25 – 27 min
deeper reason for it being such long lifetime, no pairing, shorter range (50m), low data thourghput

## Slide 2: BLE Beacon technology
Devices that broadcast small pack of data to nearby portable electronic devices.
Protocol designed to enable devices with low power consumption.
Only transmits small packets.
Long lifetime: 3~5 years
http://blog.estimote.com/post/57087851702/preorder-for-estimote-beacons-available-shipping
Estimote
http://localz.com/blog/ibeacon-ble-hardware-commercial-comparison/
Qualcomm Gimbal
GeLo
KST Particle
RedBear Beacon B1
StickNFind
Notes: Recently become popular,
BLE devices are usually called beacons, what they do is…
Protocol is designed to ...
The devices using this protocol only... So that power consuption is very low
Estimote broadcasting signal for 3~5 years
many models on the market, with cheap price, each costs several dollars
Apple/google protocol based on xxx /SDK,

## Slide 3: BLE Beacon technology application
Customer behavior analysis: Pierdicca et al. (2015)
Indoor localization: Martin et al. (2014)
Room occupancy detection: Conte et al. (2014)
http://prismdevkit.com/lesson-8-an-intro-to-estimote-beacons/
Notes: Shows typical use case
System briefly knows where you are
-This technology enables applications in several domains including ….
-serie of Use cases:
Customer can get advertisements in the entrance, do automatic checkin and rewarded with coupons,
With indoor location feature, the beacon delivers to cumster the information of the products that are close to the customter,
They can even do smooth checkout withit

## Slide 4: BLE Beacon technology
Notes: Diagram shows Typical data flow of beacons servcice
Phone needs to have internet connection
Mention what are these arrows mean, beacon to smart phone: 18 byte packets, (URL, HTML, etc)
Use some animations,

## Slide 5: How about images?
What if we want to let Beacon broadcasting images?
https://www.tes.com/lessons/S8VtfCaXvNCH4w/shapes
http://www.promarksigns.com/
https://openclipart.org/detail/223635/exit-sign
http://www.vectorportal.com/StockVectors/Icons/GREY-PRINTER-ICON/17769.aspx
https://www.iconfinder.com/icons/389375/brew_brewing_cafe_coffee_coffee_machine_coffee_maker_cup_drink_espresso_expresso_machine_maker_icon
Notes:   It will be much more useful if beacon can broadcasting images
  Motivication can be explained by this 1913 newspaper advertisement, image worth 1000 words
  Beacon that broacdasting images will provide us with opportunities that to play with images that has connection to the physical world such as …
https://en.wikipedia.org/wiki/A_picture_is_worth_a_thousand_words
TODO: cite the 1913 image

## Slide 6: How about images?
Notes: This feature is covered by the previous data flow -
Data flow for images

## Slide 7: What if there is no Internet connection?
http://www.sierraclub.org/sierra/activism/saving-wild-places?page=7
Notes: but .....
Imaging in a Wild place without internet connection, you still want to retrieve rich multimedia such as images data from beacon
This is useful because a traveller doing Hiking can write custom images presents useful information such as navigation signs into beacon
And drop the beacon
So other people come later. And it will last for years.
Surveillance camera connect to beacons taking pictures and people can use a drone can fly close to retrieve the images

## Slide 8: Store image data into Beacons
Short
delay
Lifetime: 3~5 years
No Internet connection!
Notes: -in order to implement this, we would like to have such different data flow
-and the system has the property such as Lifetime statement (years long),
- Another portable device such as a smart phone will get the image if it goes close to the beacon
-thanks to the BLE technology, receiving of the image will have short delay
-No internet connection

## Slide 9: Store image data into Beacons
Input Image
Writer
App
Reader
App
Estimote
Beacons
Notes: We implemented this system
We wrote a writer app Having an input image, we convert it into a form that is capable to be stored into three beacons
－ Smart phone app

## Slide 10: Challenge
Limited broadcasting data packet size
4 Bytes in iBeacon mode (UUID is not changeable via API)
18 Bytes using Eddystone URL mode
Future: BLE 5.0 with 8x broadcasting capacity: ~256 bytes
  -> We must compress the images
iBeacon packet format
http://www.argenox.com/bluetooth-low-energy-ble-v4-0-development/library/a-ble-advertising-primer/
Notes: TODO: find deeper hack’s memory limit
-The major challenge we face is the extremly limited storage space of BLE beacons
-Diagram iBeacon packet foramat
- With the ibeacon format and SDK, what the user can use as storage space is 4 bytes
-details: naively using the ibeacon protocol that broadcasting uuid, major and minor values, we cannot change the UUID so we only got 4 bytes each beacon
Eddystone
Deeper hack: maximum xxx bytes
A typical image with small size (64 x 64) can easily exceeds 5 thousands bytes

## Slide 11: Approaches
Limit image type
(binary image, DCOSS 2016)
Select region of interest
(color image, IoTDI submission)
Customized image compression
Notes: Another thing we can do is to constrain the image type
For each image type, there exist compression methods specifically designed for it

## Slide 12: Conventional compression is not good enough
  A typical simple shape 64x64 JPEG format image: 400 bytes ~ 2KB
  For the “Lena” image:
Default quality
8549 Bytes
Quantization
level 20
1077 Bytes
Simple threshold
637 Bytes
Default quality
1382 Bytes
Quantization
Level 20
732 Bytes
Canny
1268 Bytes
Chain
Coding:
427 Bytes
Notes: Put here: simple shape such as a image of disk it’s size
for a more complicated image such as Lena
The first row is all JPEG compression
JPEG is about tranferring signal into freq space and downsampling
Quantization is like downsampling in frequency space
What else is there besides JPEG? Backup slide ready for that.
Cite state of art color image compression codec
Tree-based image compression paper

## Slide 13: Solution
Develop a custom image compression
Binary image compression: patch based method
Color image compression: adaptive encoding
Notes: The solution is to develop a custom iamge compression technique that better fits this case
We developed a patch based method

## Slide 14: Patch-based compression
Patches are matched based on Structural Similarity (SSIM)
Beacons store / broadcast indices of patches
Notes: Each grid is similar to this patch
To geenrate the set of patches, one approach that acdtually works very well is to use spiral images
“Having one spiral does not always help,
Having an array of spirals is more effective “

## Slide 15: Patch-based compression
Set of spiral patches derived from K-means clustering

## Slide 16: Compression result
CR: compression ratio
Notes: Morphology: small island removed, connected component enhanced
Using a very trivial encoding: store all indices, the compression ratio is already very good
This plot comparison between our method and JPEG
In some areas, you can have some images what my method works better than jpeg: better quality and lower size.
Blue: you need around half a dozen or two dozen
Red: 2 or four beacons

## Slide 17: Overall Process
Notes: We generate a large population of patches using images…
When we do k means

## Slide 18: Evaluation
Varying parameters (beacon number, image type, k-means settings..)
Plot image quality vs. device lifetime.
Life time is estimated from API. We did not wait 60 months!
Notes: alpha-numerical character, shapes, images,
Lena image and xxx
Basiccaly Evaluation goal is to tune the parameters, let us understand the impact of changes of different settings
The analysis is to analyze the approximated images quality vs device lifetime. Under different settings
such as different number of beacons and image quality, different type of images, and different parameters in k-means clustering …
Setting: has to arrive in 1s
The underline logic is that different settings will result in different encoding image size, which gives the number of packets transmitted under 1s, this impacts transmission frequency, turther device lifetime

## Slide 19: Evaluation
Adding more Beacons gives a better image quality, but when the number of Beacons is larger than 3 the improvement is not significant.
Notes: This plot shows the system performance using different number of beacons

## Slide 20: Evaluation
K-means on multiple spiral patches performs better than using single spiral. K-means on MNIST patches outperforms K-means on spiral patches on the Alpha-Numeric dataset.
Notes: This shows the image approximation performance for 3 types of images, here we also tried to make a patch generated from k-menas on MNIST handwritten digit dataset
For arbitrary image, k means on spirals is better when the available data storage capacity is more limited, but it does not do better than MNIST in high frquency setting
K = 64, patch size = 8 pixels

## Slide 21
Reading-writing into Beacon
12 participants
Notes: - WE also did some user study
-Goal: Test if the user write image can be read by another one
-12 participants
-We had drawing
-Better to expand in the whole screen, not being symbols that are easy to confused with other symbols “o”

## Slide 22: Navigation test
5 participants
Notes: -Goal: simulated remote navigation / hiking system
-5 participants
- deployed 6 beacons with navigation information in 6 locations in the building’2 and 3 floor
- follow the iamges from xx to xx, displayed on the screen
- route like this
- Free to give up
Finally we ask their idea of the clearness of the signs
－ 4 of 5 participants successfully completed the route,
1 gave up because of xxx
This drags down the user’s subjective socre of image 3
we believe with more careful deploying, the technology can be useful in customized navigation without internet connection
http://cs.unc.edu/files/2013/12/brooksbuildingsmall.jpg

## Slide 23: Color image: approach
Region of interest
  Foreground, adaptive encoding:
    DCT
    Wavelet
    Triangle mesh
  Background:
    Down sample -> DCT
Notes: Region of interest: foregorund / background
Allocate more bits describe the foreground
Still needs to preserve the background to give some context info

## Slide 24: Segmentation
Generating an accurate segmentation
Apply a good encoding method for foreground region
Notes: Single image-based, segmentaiton, such as watershed based method some times are not accurate,
Depth based method requires multiple view caputre, tends to be noisy
Combine the two results

## Slide 25: Image encoding
Reduce frequency component coefficients / quantization
Reduce mesh density
Notes: Foreground and background processed separately
We would like to control the size/quality of the foreground, For DCT wavelet, reducing the frequency compoent coeffs, for triangulariztio, we can reduce mesh desity

## Slide 26: System
How to find a good pair of images?
- Use IMU signal
Notes: Here we have another optimization here: the good pair of images may not be easy to find: the user may need to try many times.
We design and implemented a IMU guided capture

## Slide 27: Evaluation
IMU-guided view capture
  Sensor readings: rotation vector, acceleration vector
  Train a decision tree model
  Use the model and IMU reading to predict the good pair of images
Notes: Reduce the time of find a good pair of images,
Training phase, we record the sensor data, labeled each one by the depth map qualty
Train decision tree model
Use to predicdt the good pair of iamges

## Slide 28: Evaluation
Notes: Contains road signs, buildings, indoor / outdoor bojects

## Slide 29: Evaluation
Notes: Green color curve: jpeg, Beat jpeg again

## Slide 30: Evaluation
Varying image type
Varying number of
beacons
Notes: :Plot 1 shows building images has larger part as foregrorund, this makes it cost more energy to deliver a good quality
Plot 2 Similar to the binary iamge case,

## Slide 31: Evaluation (User Study)
Recognize objects
Notes: Have four group of objects
Compress image of one object in every group,
Let participant guess which one it is

## Slide 32: Future work
GIF images, videos
“Fat beacon”
Notes: Could surrport GIFs or other videos
Beacon community and people in Google are talking about deveoping the fact beacon standard that is for storing/broadcatsing webpages inside beacon,how our method work with it may be a research topic (thumbnails)

## Slide 33: Thank you Questions?

## Slide 35: State of art image compression
JPEG2000
HEVC-MSP
https://people.mozilla.org/~josh/lossy_compressed_image_study_october_2013/
http://www.compression.ru/video/codec_comparison/wmp_codecs_comparison_en.html

## Slide 36: SSIM

## Slide 37
Notes: #2. explain with a plot or numbers why BLE last multiple years (energy saving technology)
#3. Reference papers [X, Y, Z] perhaps.
#4. Name the arrows (add text to explain what each arrow means)
#5. More kinds of images: signs? real photos? shapes?
#7. More examples of usages?
#8. Mention lifetime requirement, mention no Internet required.
#9. Little more description/annotation
#10. Write iBeacon if it is.
#11. Add example images.
#12. Mention the quality number, what is changed? Is the last one your technique?
#13. SSIM metric here?
#14. Show an image and mark the patches - maybe an example: image -> patch numbers
#16. Define SSIM, CR; mark the gap between compression ratios
#19. Make 2 separate slides; Add a 'conclusion line' below each plot
#20. More on deplyoment setup: number of people, images, beacons, etc. Mention the goal of this experment: update the slide title.
#21. Add drawings -- arrows etc. Mention the goal of this experment: update the slide title.