## Slide 1: Generic Framework for Prioritizing Content of Interest in Multimedia Data Compression
Chong Shao
University of North Carolina at Chapel Hill
Advisor: Shahriar Nirjon, Russell Taylor
Notes: Give a practice talk about my research, as a practice talk for defense
The title is …
TODO: complicate contribution slides, so people understand what’s new
XXX details about H.264: how it handles the region of interest ?????
XXX may add a backup slide for sliding window
Xxx read the nature paper
Xxx read the microscopy paper
TODO: page 44 explanation
TODO: a slide for adding noise
TODO: update slide 70 for the distance between the gaussian
TODO: more formula about localization can be added
TODO: update page 15 equations
TODO: explain the evaluation: how these things are linked
TODO: page 60, why huffman coding is H?
TODO: maybe a slide talk about adding synthesized noise into video
TODO: page 43 may add the benchmark plot
https://www.statista.com/chart/3780/tv-screen-size/
http://drpeering.net/white-papers/Internet-Transit-Pricing-Historical-And-Projected.php
http://blog.dshr.org/2016/05/talk-at-seagate.html
http://blog.dshr.org/2014/03/the-half-empty-archive.html
http://ieeexplore.ieee.org/xpl/login.jsp?tp=&arnumber=6269460&url=http%3A%2F%2Fieeexplore.ieee.org%2Fxpls%2Fabs_all.jsp%3Farnumber%3D6269460
http://dl.acm.org/citation.cfm?id=290814
http://ieeexplore.ieee.org/xpl/login.jsp?tp=&arnumber=4387595&url=http%3A%2F%2Fieeexplore.ieee.org%2Fxpls%2Fabs_all.jsp%3Farnumber%3D4387595

## Slide 2: All compressions

## Slide 3: What is beacon
Diagram of a beacon, EM waves, and a short packet, URL, receiver

## Slide 4: Motivating example
Store image data into Beacons (30 bytes storage)
http://www.sierraclub.org/sierra/activism/saving-wild-places?page=7
Notes: The central idea about my research is the notion of extreme compression
The discussion is on compression on multimedia data, including images and videos
It is meaningful to consider the problem because …
a person doing hiking can put custom graphical navigation
info
a beacon attached to camera can work as long lifetime survelliance broadcasting system without human intervention

## Slide 5: Extreme compression: image
Notes: For images, we have all kinds of compression technologies including … / … and … to reduce the data size,
But all common compressions method, on a 64x64 image, using the lowest quality setting, the smallest compressed file size you can get is about 1000 bytes,
To the best of our knowledge, no one has considered design color image compression method to compress data below 1000 bytes.

## Slide 6: Motivating example
Compressing microscopy videos
High throughput microscope
Storage
Analysis program
Notes: The second example is..
The data consumption pipeline for the microscpy video is,
Firly multple videos are captured by the highthoughput microscope system,
Then it is stored in disk, followed by an routine that running video analysis algorithms and derive results

## Slide 7: Extreme compression: video
Notes: Same thing happens for video,
[there is 100x compression available, but for PSNR < xxx, means to have it actually useful, ]
usually people design video codecs [takes into performance (compression ratio, video quality, compression time) different options (many parameter you can tune) & simplicity ( easy to impelemnt ) into account,] usually achieves 40%~10% compression ratio. Which is not sufficient for the microscopy system

## Slide 8: Problem of interest
For systems with limited storage, conventional techniques sometimes fail to provide sufficient compression.
Develop a new approach to achieve better compression than conventional compression techniques.
Notes: So the problem of interest of my research is …
The goal is to ///

## Slide 9: Approach
Traditional:
L(x) = H – f(x)
New:
L(x) = f’(x)
Information to reduce
Information to keep
Entropy
Notes: Even though the question in two given examples look different, they can be addressed in the same way
The basic idea of my approach is shown in the plot
instead of following the traditional compression method that reduces the amount of information in the input data,
We construct the compressed data by prioritizing the content of interest.
Then we can have a new formula the data size of the compression

## Slide 10
Prioritizing the content of interest in systems with extreme storage limit and application-specified quality requirement leads to new compression algorithms that give better compression ratio than standard methods with the same quality compressed data for the application.
Research statement
Notes: Therefore my thesis statement is:
[I looked into the systems I worked on and find out the type of system where new compression works better is when why traditional compression techniques does not work efficiently,
The reason is that there are mismatches exist in the systems, for example … ]

## Slide 11
Today’s talk
Microscopy video compression
Multimedia data compression for Bluetooth low energy beacons
Notes: Today’s talk includes two aspects of my research, the compression on microscopy videos, and the multimedia data compression for Bluetooth low energy beacons, this slide shows the hardware and some sample data for both systems

## Slide 12
Microscopy video compression
Microscopy video compression
Multimedia data compression for Bluetooth low energy beacons
Notes: I will first talk about microscopy video compression

## Slide 13
Increase in the amount of video data is faster than the increase in affordable data storage.
http://cismm.cs.unc.edu/core-projects/force-microscopy/high-throughput-microscopy/
Background
Notes: Mordern Microscopy systems with multiple channels that can generate multiple high resolution videos in short time
The system shown in the right is a 12 channel microscope in. the physics department, can generate 1TB video in a hour
The problem in the system is

## Slide 14: Video Compression
Require that the compression has no impact on analysis -- scientifically lossless
Standard (H.264) lossy compression techniques cannot be used
Standard lossless compression technique yields the compressed data in the size of 49.74% of the original one
Our method gives: 7.26%
Best case: 0.7729% vs. 19.4505%
Notes: This shows a sample video,
The constraint on the video compression is that,
Standard ... cannot be used as when it is set to lossless mode, the compression ratio is not high enough for the system

## Slide 15
Method | Making use of temporal reduction | Compression ratio
JPEG | No | ~4
H.264 | Yes | ~5
Bernas et al. | No | ~9
Our method | Yes | ~100
Bernas T, Asem EK, Robinson JP, Rajwa B. 2006. Compression of fluorescence microscopy images based on the signal-to-noise estimation, Microsc. Res. Tech., 69: 1–9. doi: 10.1002/jemt.20259
Related work
Notes: This shows the related work, and our method can achieve far more better compression than existing approaches

## Slide 16: Approach
The capture side captures the entire frame, the viewer side only uses pixels in ROI
ROI
Notes: Our method makes use of the fact that not all pixels from the captured video is used in the analysis
The left is a region of the sample video frame while only the white region on the right side is used in analysis.

## Slide 17: Approach
Store only the information in a video that analysis can use
Separate every frame into foreground (pixels that carry information) and background (pixels that do not change throughout the video).
Average out noise in the background. -> easy to compress
Losslessly compresses the foreground regions
Notes: The approach is …
Generate a new video by replacing every background pixel by its average value over time,
Compress the new video using standard lossless techniques
Since many of the pixels are constant over time in the new video, it will be easier to compress
The question left is How to tell a pixel F/B?

## Slide 18: Key Observation
http://en.wikipedia.org/wiki/Point_spread_function
Gaussian
Poisson
1. In the microscope image formation process, convolution with the point-spread function spreads image brightness changes in one pixel to its neighbors.
-> neighboring foreground pixels’ intensity over time values are correlated
2. The noise is independent between neighboring pixels.
Notes: For identify foreground,
We can make use these two properties in a microscopy video
Foregorund pixel is after the convolution
->
Background is pure noise

## Slide 19
Pearson’s correlation based method
Foreground / background separation
High score: foreground
Notes: We can use correlation for segmentation
compute the correlation score of everypixel and its adjacent pixels over time
We take the mangnitude of the eight correltaion values,
And use the largest one as the score assigned to the center pixel
Higher score will suggest that it is foreground

## Slide 20
Video
Plot of scores
Binary map
Foreground / background separation
Notes: We can do some thresholding on the scores to generate a binary map with the white region indicating the foregrounds

## Slide 21: Refine the result: Key Observation
1. the noise is independent between neighboring pixels
2. convolution with the point-spread function present in the microscope image formation process spreads image brightness changes in one pixel to its neighbors.
-> Small “islands” should not be foreground, remove
Notes: Tends to be noisy, we add a refinement stage to clean it up
The reasoning behind that is that
Because we know the existing of point spread function is larger than 2 pixels
and the noise is independent between neighboring pixels
Which means that, in the binary map, the small while islands of one or two pixels should not be foregound and they should be removed

## Slide 22
Video Spot Tracker
Notes: Also we would like to include some background, for application purpose.
In doing analysis on the object movement, we use the software video spot tracker
The software tracks the object by placing a tracker centered at the object
The tracking analysis does not only take the foreground pixels into account, also some background pixels inside the tracker

## Slide 23: Refine the result Mathematical Morphology
erosion
dilation
3 x 3 pixels
Fit tracker size
Notes: Given a binary map, we want to remove the small white regions, we use a erosion operation with operator size 3x3 pixels, which removes the white islands smaller than t3x3 pixels
After the erosion, we dilate the result using a dilation operator with the size fit the tracker size, which will expand the foreground regions, then all the pixels that the video spot tracker uses in analysis will be losslessly compressed

## Slide 24: Overall approach
Video Size: L(x) = L(x’) + c
Required bit length for lossless encoding foreground
Required bit length for encoding background
Notes: This is shows the overall approach of the compression technique
Having the binary map, we refine it, we use the refined binary map to generate a new video which has background pixels replaced by their averages over time
This video will be better compressed than the original video, we can also run the analysis to the check if it has the same result as the original video
The video data bit length can be formulated as the required bit length for the foreground pixels and a small term for encoding the background.

## Slide 25
Experiments
Notes: In evaluation my method, I used four videos, contains different number of beads and different lighting conditions

## Slide 26: Results 1: compression ratio
(Using hard coded threshold)
Notes: Horizontal axis: different threshold for segmentation used , Vertical axis, Horizontal lines, Dotted line
solid… means with this threshold, the compression has no impact on analysis
Lines in the same color means they are using the same video
In all four cases, our method always outperforms standard method,
Arrow: more than 100x

## Slide 27: Result: compression ratio
 | Video 1 (Beads 1μm) | Video 2 (Beads 500nm) | Video 3 (Brightfield 1) | Video 4 (Brightfield 2) | Video 5 (Cells)
H.264 | 20% | 28% | 47% | 50% | 33%
Our method | 0.77% | 20% | 44% | 7.3% | 4.8%
Notes: This is the table version of the same experiment result

## Slide 28: Quickly moving foreground objects
Notes: In practice, we have videos that...
We have to label a pixel as foreground if is on the trajectory of the object movement, in total most of the pixels are marked as foreground

## Slide 29: Sliding window
Window size?
Notes: To make our method works more efficiently on this type of video
We do the correlation analysis based on the frames in the windows
and store the frames based on the binary map generated in this analysis in the window
when the foreground objects stay static, we don’t have many pixels marked as foregound,
Gives us a chance to better compress the video
Question is size

## Slide 30
Sliding window
Notes: Explain the table
You can expect the smaller window size is better than the larger one,
But the too small window size will make the background pixel average value keeps changing, this will make the result video to be harder to compress
Experiment shows that 10 frames window size gives the best compression result

## Slide 31: Analysis-aware compression
We can do better if we allow lossy compression (compression changes the analysis result on the video)
Notes: Also, the is still space for improvement,
[read]
which leads to another type of compression method called analysis aware compression

## Slide 32: Analysis-preserve vs analysis-aware
The analysis result (vertical line) on the actual object motion is the ground truth
The actual video contains noise that makes the analysis result a random variable that follows a probability distribution
The analysis result on compressed video is also a random variable that follows a probability distribution
Notes: To understand this argument,
Firstly consider the analysis is about analyze object motion in the video
If statistically these two sets of result come from the same distribution, then the compressed video is still useful

## Slide 33: Analysis-aware compression
KS test
KL divergence
Empirical distribution function
Notes: In testing if two set of samples come from the same distribution, we uses two methods, KS test, and KL divergence
KS test is basically …
KL divergence tells.

## Slide 34: Analysis-aware compression
Video Size: L(x) = L(x’) + c
Required bit length for lossless encoding foreground
Required bit length for encoding background
Notes: Here the bit length for the compressed video is formulated the same as the one for the previous technique.
The difference in the pipeline is that, we add synthesized noise into the compressed video.
we finally send the analysis result into a set of statistical tests
We did experiments on synthetic video and real video, in synthetic video, we know the true object positions, and we generate noisy video based on that

## Slide 35: Analysis-aware compression
Notes: In real video, we don’t know the true object positions, so we divide an input noisy video into multiple segments to generate a population

## Slide 36: Evaluation (generated data)
KS test
KL divergence
Notes: I implemented two versions of Analysis-aware compression, one reduces the video information by avaraging background pixels, second change H.264 codec to assign background low qulaity values. The expeirment also compares the result with and without adding synthesized noise as post-processing
Horizontal axis is ...
vertical axis is ...

## Slide 37: Evaluation (real video)
KS test
KL divergence
Notes: For the real video, H264 also works in the most of time, but from the right plot, we can see for small compression ratio, we get better result on our method

## Slide 38: Method summary
Compression method based on correlation followed by mathematical morphology can give at most 100x compression
  Extension: sliding window
Analysis-aware compression evaluates microscopy video quality using statistical tests
  Enables even higher compression ratio

## Slide 39
Novelty:
Microscopy video compression with 100x compression ratio
A new correlation-based microscopy frame segmentation technique based on point spread function
A new way to evaluate the quality of a microscopy video based on statistical test
How to generalize:
Correlation based segmentation can be applied to imaging devices including microscopes, telescopes, and other cameras where the object is not perfectly in focus
Adding synthesized noise to improve the video quality can be applied to videos other than microscopy.
Contributions (microscopy video compression)
Notes: The contribution of this work includes
The invented segmentation method can be generalized to …

## Slide 40
Multimedia data compression for Bluetooth low energy beacons
Microscopy video compression
Multimedia data compression for Bluetooth low energy beacons

## Slide 41
Devices that broadcast small pack of data to nearby portable electronic devices.
Protocol designed to enable devices with low power consumption.
Only transmits small packets.
Long lifetime: 3~5 years
Background: BLE Beacon technology
http://blog.estimote.com/post/57087851702/preorder-for-estimote-beacons-available-shipping
Estimote
http://localz.com/blog/ibeacon-ble-hardware-commercial-comparison/
Qualcomm Gimbal
GeLo
KST Particle
RedBear Beacon B1
StickNFind
Notes: Firstly briefly go over what is a BLE beacon
Devices broadast data using Bluetooth low energy protocol
Upper level protocol build upon it

## Slide 42: Background: BLE Beacon technology application
http://prismdevkit.com/lesson-8-an-intro-to-estimote-beacons/
Notes: Shows typical use case
System briefly knows where you are
-This technology enables applications in several domains including ….
-serie of Use cases:
Customer can get advertisements in the entrance, do automatic checkin and rewarded with coupons,
With indoor location feature, the beacon delivers to cumster the information of the products that are close to the customter,
They can even do smooth checkout withit
Customer behavior analysis: Pierdicca et al. (2015)
Indoor localization: Martin et al. (2014)
Room occupancy detection: Conte et al. (2014)

## Slide 43: Why store multimedia data into beacon devices?
  Google Physical Web, Fat Beacon
  Beacon deployment for places without Internet connection
Notes: Our goal is to have a different usage of the beacon devices
Why we need to ..?
Since there is plan to make beacons more powerful, Google is working on the concept of Fat beacon store broadcast webpages, as part of the physical web project,
Multimedia contensts such as Images can be an important part of a webpage
While we want to deploy beacons into places without internet connection, and we want to broadcast multimedia data, for example, shown in the early part of the talk, outdoor survelliance

## Slide 44: Challenge: Battery Life constraint
Notes: The challenge of doing it is that, for a large trunk of data, even though we can let beacon to broadcast part of the data in one period,
The beacon broadcast frequency has impact on beacon battery life,
For too large data size, we either have to wait for a long time, or we have to sacrifice beacon battery lifetime
https://files.readme.io/m5rzEic2TcyB3k1HLrQw_beacon_energy_consumption.png

## Slide 45: Challenge: Battery Life constraint
Notes: TODO

## Slide 46: Challenge: BLE packet format
Limited broadcasting data packet size
4 Bytes in iBeacon mode (UUID is not changeable via API)
18 Bytes using Eddystone URL mode
30 bytes using BLE lower level protocol
Future: BLE 5.0 with 8x broadcasting capacity: ~256 bytes
  -> We must compress the data
iBeacon packet format
http://www.argenox.com/bluetooth-low-energy-ble-v4-0-development/library/a-ble-advertising-primer/
Notes: The other side of the challenge is that the beacon packet format limits the data size to be 30 bytes, which means that we need many broadcasting cycles for 1000 bytes data

## Slide 47: Challenge: traditional compression is not good enough
  A typical simple shape 64x64 JPEG format image: 400 bytes ~ 2KB
  For the “Lena” image:
Default quality
8549 Bytes
Quantization
level 20
1077 Bytes
Simple threshold
637 Bytes
Default quality
1382 Bytes
Quantization
Level 20
732 Bytes
Canny
1268 Bytes
Chain
Coding:
427 Bytes
Notes: JPEG is about tranferring signal into freq space and downsampling
Quantization is like downsampling in frequency space
What else is there besides JPEG? Backup slide ready for that.
Cite state of art color image compression codec
Tree-based image compression paper

## Slide 48: Projects
Constraint data type,
binary image (DCOSS 16)
Color image
make use of hardware (IOTDI 17)
3D motion data, visual feature data (MARBLE)
Notes: I will talk about three projects I did on BLE beacons, with my custom compression techniques

## Slide 49
Method | Binary Image | Color Image | Result small enough for BLE
Chain-coding | ✔ | ✖ | ✔
JPEG | ✔ | ✔ | ✖
Shapiro et al. | ✔ | ✔ | ✖
Lu et al. | ✔ | ✔ | ✖
Our method | ✔ | ✔ | ✔
Related work
Notes: Our method is the one that gives result small enough for BLE and supports color image
This table shows the related work. Including some other image compression tec
Jerome M Shapiro. 1993. Embedded image coding using zero trees of wavelet coeffcients.IEEE Transactions on signal processing41, 12 (1993), 3445–3462
Tianyu Lu, Zisheng Le, and DYY Yun. 2000. Piecewise linear image coding using surface triangulation and geometric compression. In Data Compression Conference, 2000. Proceedings. DCC 2000. IEEE, 410–419
hniques

## Slide 50: Binary image: approach
Patches are matched based on Structural Similarity (SSIM)
Beacons store / broadcast indices of patches
Notes: Each grid is similar to this patch
To geenrate the set of patches, one approach that acdtually works very well is to use spiral images
“Having one spiral does not always help,
Having an array of spirals is more effective “

## Slide 51: Patch-based compression
Set of spiral patches derived from K-means clustering
Image size: L(x) = L(g(K Log(D)))
Number of patches
Patch bank size

## Slide 52: Compression result
Notes: Morphology: small island removed, connected component enhanced
Using a very trivial encoding: store all indices, the compression ratio is already very good
This plot comparison between our method and JPEG
In some areas, you can have some images what my method works better than jpeg: better quality and lower size.
Blue: you need around half a dozen or two dozen
Red: 2 or four beacons

## Slide 53: Overall process
Notes: The overall process has an offline phase and an online phase

## Slide 54: Evaluation
Varying parameters (beacon number, image type, k-means settings..)
Plot image quality vs. device lifetime.
Life time is estimated from API. We did not wait 60 months!
Notes: alpha-numerical character, shapes, images,
Lena image and xxx
Basiccaly Evaluation goal is to tune the parameters, let us understand the impact of changes of different settings
The analysis is to analyze the approximated images quality vs device lifetime. Under different settings
such as different number of beacons and image quality, different type of images, and different parameters in k-means clustering …
Setting: has to arrive in 1s
The underline logic is that different settings will result in different encoding image size, which gives the number of packets transmitted under 1s, this impacts transmission frequency, turther device lifetime

## Slide 55: Evaluation
Adding more Beacons gives a better image quality, but when the number of Beacons is larger than 3 the improvement is not significant.
Notes: This plot shows the system performance using different number of beacons

## Slide 56: Evaluation
K-means on multiple spiral patches performs better than using single spiral. K-means on MNIST patches outperforms K-means on spiral patches on the Alpha-Numeric dataset.
Notes: This shows the image approximation performance for 3 types of images, here we also tried to make a patch generated from k-menas on MNIST handwritten digit dataset
For arbitrary image, k means on spirals is better when the available data storage capacity is more limited, but it does not do better than MNIST in high frquency setting
K = 64, patch size = 8 pixels

## Slide 57: Navigation test
5 participants
Notes: -Goal: simulated remote navigation / hiking system
-5 participants
It has an animation!!!!!
- deployed 6 beacons with navigation information in 6 locations in the building’2 and 3 floor
- follow the iamges from xx to xx, displayed on the screen
- route like this
- Free to give up
Finally we ask their idea of the clearness of the signs
－ 4 of 5 participants successfully completed the route,
1 gave up because of xxx
This drags down the user’s subjective socre of image 3
we believe with more careful deploying, the technology can be useful in customized navigation without internet connection
http://cs.unc.edu/files/2013/12/brooksbuildingsmall.jpg

## Slide 58: Color image: approach
  Foreground, adaptive encoding:
    DCT
    Wavelet
    Triangle mesh
  Background:
    Down sample -> DCT
Notes: Region of interest: foregorund / background
Allocate more bits describe the foreground
Still needs to preserve the background to give some context info

## Slide 59: Data size
Image Size: Ldct(x) = L(g(ddct(x))) + c
Required bit length for encoding foreground in DCT
Required bit length for encoding background
Lwavelet(x) = L(H(dwavelet(x))) + c
Required bit length for encoding foreground in wavelet
Required bit length for encoding background
Lmesh(x) = L(g(v(x), n(x), i(x))) + L(g(t(x))) + c
Required bit length for encoding vertices, texture index, connections
Required bit length for encoding background
Required bit length for encoding the texture
Notes: Gzip: LZ77, dictionary based compression
For different encoding method, the formula is different, and they all follows the framework of contructing the data from the content of interest

## Slide 60: Segmentation
Generating an accurate segmentation
Apply a good encoding method for foreground region
Notes: Single image-based, segmentaiton, such as watershed based method some times are not accurate,
Depth based method requires multiple view caputre, tends to be noisy
Combine the two results

## Slide 61: System
How to find a good pair of images?
- Use IMU signal
Notes: Here we have another optimization here: the good pair of images may not be easy to find: the user may need to try many times.
We design and implemented a IMU guided capture

## Slide 62: IMU-guided multi-view capture
Sensor readings: rotation vector, acceleration vector
Train a decision tree model
Use the model and IMU reading to predict the good pair of images
Notes: Reduce the time of find a good pair of images,
Training phase, we record the sensor data, labeled each one by the depth map qualty
Train decision tree model
Use to predicdt the good pair of iamges

## Slide 63: Image encoding
Reduce frequency component coefficients / quantization
Reduce mesh density
Notes: Foreground and background processed separately
We would like to control the size/quality of the foreground, For DCT wavelet, reducing the frequency compoent coeffs, for triangulariztio, we can reduce mesh desity

## Slide 64: Evaluation
Notes: Contains road signs, buildings, indoor / outdoor bojects

## Slide 65: Evaluation
Notes: Green color curve: jpeg, Beat jpeg again

## Slide 66: Evaluation
Varying image type
Varying number of
beacons
Notes: :Plot 1 shows building images has larger part as foregrorund, this makes it cost more energy to deliver a good quality
Plot 2 Similar to the binary iamge case,

## Slide 67: Evaluation (user study)
Recognize objects
Notes: We take a image on an object in the lab, compresed it, and mix the object with similar objects,
Then we ask the participant to look at compressed image. guess which one it is,
We repeat the experient with 4 group of objects,
And record the correct guesses
For the higher storage space, we allow higher quiality images, imporves the chance of correct guess
Object with spatial tetxure is easy to recoginize

## Slide 68
Another project: augmented reality
Beacons
Cameras
Object of interest
Viewer’s device
Virtual object
Notes: I did another example in using ble beacons for incdoor agumented reality
The sytem wroks in two phases
In capture phase, the object of interest is captured by the camera placed in the room, the motion data is recoreedd and sostred in the beacons
Then in the render phase, a reviewr can use a mobile phone or tablet to receive the data from beacon and watch the virtual object rendered in the scene

## Slide 69: Data to store in the system
3D motion avatar
Localization
  IMU camera rotation/acceleration data
  Camera visual feature data
  BLE signal strength
  Sensor fusion
Notes: This shows the system in action. The person is captured and rendered as an avator composed by simple shapes
We need to do localizatoin and pose estimation of the viewer, in order to doing that, we also need to put additional data into the beacon
Xk: estimation of the status
Fk: relationship
Pk: Convariance
Bkuk: outside influence
Qk: outside influence on convariance
Hk: sensor reading scaling
Rk: uncertainty of sensor
Zk: observed new measurement
K’: kalman gain

## Slide 70: Visual feature selection
Reducing the number of features
Notes: We need to store visual feature data into beacons, to reduce the data size, we only select the subset of the visual feature. Detected. IN the selection, we consider the two factors, the entropy of the feature and the location of the feature in the image. We prefer visual feature with high entropy and more close to the center of the scene, the reason for the first factor is that we want to reduce the chance of mismatch, the reason for the second factor is that the image being matched is usually shoot in the same scene as the reference image

## Slide 71: Data size
L(x) = L(t*k*n) + L(f) + c
Required bit length for encoding 3D motion data
Required bit length for encoding camera metadata
Required bit length for encoding visual features
Notes: The size of the data to be stored in the beacon can be contains three parts, the … which is related to how may key points, the data size for each key point and the length of the 3D motion, it also includes the data size for encoding visual feature and the data length for encoding camera metadata, position and focal length, etc.

## Slide 72: Evaluation
Notes: In evaluation, we measure the localization error in centermeters and pose estimation accuracy in angles
we compare the result with only use BLE, only use camera and with sensor fusion
Result is shown in heat map
Our system will turn off camera matching when the viewer’s camera is not looking at the scene where the virrtual object is placed, so the are two missing measurements.
Result suggests that, sensor fusion will improve the accuracy in both localization and pose emstimation in most cases

## Slide 73: Method Summary
Three new systems for multimedia data storage / broadcast via BLE
Identify the content of interest
Make use of hardware (multi-view capture for segmentation, IMU-guided capture, localization with received signal strength indicator)
Notes: TO summarize
I explained…
They used the approach of
They also makes use spatial property of system hardware, for example

## Slide 74
Novelty: enable multimedia data storage/broadcasting on systems with extreme memory/bandwidth limit.
  First BLE image broadcasting system
  IMU-guided multi-view capture algorithm
  First BLE 3D motion data recording and broadcasting system
  Visual feature selection algorithm based on region of interest and entropy
  First indoor localization system using sensor fusion that uses BLE signal
Contributions (multimedia data compression for BLE)
Notes: The contribution of this part of my research is that I built the first system for storing / broadcasting xxx, first … and first …
Algorithmwise, I designed the new visual feature selection algoirthm and IMU guided multi-view catpure algorithm

## Slide 75
How to generalize:
  IMU-guided multi-view capture algorithm can be applied in other multi-view capture systems
  Visual feature selection algorithm can increase the efficiency in any systems that uses visual features
Contributions
Notes: The IMU-guided multi-view capture method can be applied in other multi-view capture systems
Visual feature selection algorithm can increase the efficiency in any systems that uses visual features

## Slide 76
I explained framework for extreme data compression
The compression techniques uses the same approach: prioritizing content of interest
Illustrate the idea with two examples: microscopy video compression and image/3D virtual object compression for BLE
Conclusion
Notes: OK

## Slide 77
Published:
1. Shao, C., Zhong, A., Cribb, J., Osborne, L. D., O'Brien, E. T., Superfine, R., ... & Taylor, R. M. (2015). Analysis‐preserving video microscopy compression via correlation and mathematical morphology. Microscopy research and technique, 78(12), 1055-1061.
2. Shao, C., Nirjon, S., & Frahm, J. M. (2016, May). Years-Long Binary Image Broadcast using Bluetooth Low Energy Beacons. In Distributed Computing in Sensor Systems (DCOSS), 2016 International Conference on (pp. 225-232). IEEE.
3. Shao, C., & Nirjon, S. (2017) ImageBeacon: Broadcasting Color Images over Connectionless Bluetooth LE Packets. In Proc. of 2nd IEEE International Conference on Internet-of-Things Design and Implementation (IoTDI 2017), 12 pg,
Under Submission/In Preparation:
4. Shao, C., Cribb, J., Osborne, L. D., O'Brien, E. T., Superfine, R., ... & Taylor, R. M. Analysis‐aware video microscopy compression, Microscopy research and technique
5. Shao, C., Islam, B., & Nirjon, S. MARBLE: Mobile Augmented Reality Using BLE Beacons
Other work as coauthor:
6. Cribb, J.A., Osborne, L.D., Beicker, K., Psioda, M., Chen, J., O’Brien, E.T., Taylor II, R.M., Vicci, L., Hsiao, J.P.L., Shao, C. and Falvo, M., 2016. An automated high-throughput array microscope for cancer cell mechanics. Scientific reports, 6.
Papers

## Slide 78
Thank you!
Questions?
Notes: OK

## Slide 79
Mismatches between video/image generator and consumer start to appear in modern multimedia systems that make current compression strategy inefficient.
Prioritizing the content of interest in these systems leads to new compression algorithms that give better compression ratio than standard methods with the same quality compressed data for the application.
Thesis statement
Notes: I looked into the systems I worked on and find out the type of system where new compression works better is whenwhy traditional compression techniques does not work efficiently,
The reason is that there are mismatches exist in the systems, for example …
Therefore my thesis statement is:

## Slide 80: Analysis-aware compression
potentially useful
Notes: Since the noise already changes the analysis result, if a statistical test cannot tell the difference of the difference introduced by compression and the difference introduced by noise, we consider the compressed video is still useful.

## Slide 81
Reading-writing into Beacon
12 participants
Notes: - WE also did some user study
-Goal: Test if the user write image can be read by another one
-12 participants
-We had drawing
-Better to expand in the whole screen, not being symbols that are easy to confused with other symbols “o”

## Slide 82
Two kinds of comparisons:
  Keep it scientifically lossless
    Compare based on compression ratio
  Having the same compression ratio
    Compare based on video quality
Experiments
Notes: Compare our method against standard lossless compression method in terms of compression ratio
Compare our method against other lossy compression method in terms of compressed video quality

## Slide 83: Video
XXX: will insert a video of the image beacon system.
Notes: Here we have another optimization here: the good pair of images may not be easy to find: the user may need to try many times.
We design and implemented a IMU guided capture

## Slide 84: Background
Data Acquisition
Data Consumption
Storage
&
Transmission
Notes: TODO: may replace with other diagram.. Think about it

## Slide 85
Correlation based method
    Given a score how to tell it is foreground or background?
Foreground / background separation

## Slide 86
Percentage based method (25%)
Foreground / background separation